CHIEF JOSEPH TDG FOREBAY	 	 		DATE COMPILED: April 3, 1998 AL

Revised: April 28, 1998 SWM

STATION LOCATION: at river mile 545.2, on left side of dam

DATA SOURCE: USACE, Northwestern Division, Portland, OR; data collected by the Seattle District

BEGINNING DATA: May 15, 1984	ENDING DATA: Sept. 13, 1997	UNITS: Celsius

DATA DESCRIPTION: From 1984-90, hourly values, 5-16 times per day; total of 11,175 values. From 1991-97, hourly values for each hour; total of 34,541 values. Daily data file from 1984-97 is 2,238 values.

Daily data file includes maximum, minimum, and mean daily values and the variability for the day.

TITLE OF FILE: Daily data: chj_tdg84-97d.xls		STATION CODE: CHJ

Hourly data: chj_tdg84-97.xls

COMPLETENESS OF RECORD:

START		END		COMMENTS			Suspicious Record

5/15/84 -------------- 7/31/84	5-7 hourly values per day

10/15/84 ----------- 11/30/84	9-16 hourly values per day

3/7/85 ---------------- 9/26/86	5-12 hourly values per day

4/21/87 ---------------- 9/3/87	7-12 hourly values per day

4/22/88 -------------- 9/19/88	6-12 hourly values per day

4/6/89 ---------------- 9/12/89	5-10 hourly values per day

4/16/90 -------------- 9/13/90	6-11 hourly values per day

missing 1991 and 1992 data

4/15/93 ------------- 10/12/93	24 hourly values per day

3/4/94 ----------------- 4/9/94	24 hourly values per day

5/5/94 ---------------- 9/21/94	24 hourly values per day		Data biased –2oC to –1oC.

5/3/95 ---------------- 9/26/95	24 hourly values per day

4/1/96 ---------------- 9/16/96	24 hourly values per day

5/5/97 --------------- 12/31/97	24 hourly values per day

VARIABILITY:

Variability is within 0.5oC most of the time.  During the summer season, when there is regulation upstream and variable heating from the sum, the variation within a day can be as great at 0.8oC.

BIAS:

Records with 0.0oC value, > 2 times adjacent values, and negative values have been removed. March 7, 1985 through March 25, 1985 appears to be biased –2.0oC. May 5, 1994 through September 21, 1994 appears to be biased from –2.0oC to –1.0oC. Data collected in the forebay are generally slightly cooler

(–0.2oC) than temperature data collected in the scroll case for most of the April-September periods.

REPRESENTATIVE OF CROSS SECTION:

Pacific States Marine Fisheries Council (PSMFC) data for 1973 shows no bias between the powerhouse and spill sides of the forebay.  There is some indication of vertical differences in June, July, and September, with the largest amounts being in July at 2.0 oC.  In the Chief Joseph tailrace, the water temperature in 1972 obtained from PSMFC is sometimes a little higher (.1- .3 oC) higher on the powerhouse side relative to the spill side

GENERAL COMMENTS:

Data are collected at a minimum depth of 15 feet. The record is generally collected seasonally from April to September. It is estimated to be within +0.5oC of the mean for the cross section except for the periods March 7-25, 1985, and May 5-September 21, 1994.