COLUMBIA RIVER AT VERNITA BRIDGE NEAR PRIEST RAPIDS DAM, WA

DATA COMPILED: Apr. 13, 1998 SWM

Revised: May 8, 1998 AL

STATION LOCATION: at river mile 388.1, on State Highway 24 Bridge at Vernita, WA, on right bank.

DATA SOURCE: USGS, Washington District, Tacoma, WA

BEGINNING DATA: Jul. 10, 1974		ENDING DATE: Sept. 30,1980	UNITS: Celsius

DATA DESCRIPTION: Daily minimum and maximum values during the 1974-75 water years and daily minimum, mean, and maximum values during the 1976-80 water year; total of about 6,370 values.

TITLE OF FILE: cr-priest.dat			 STATION NUMBER: 12472900

COMPLETENESS OF RECORD:

START		           END	COMMENTS

7/10/74  --------------- 11/17/75	daily record

11/21/75  ------------- 11/15/76	daily record

11/24/76 ----------------- 6/4/78	daily record

7/11/78  -------------- -12/14/78       	daily record

1/16/79 ------------------- 4/4/79	daily record

4/12/79 ----------------- 9/30/80	daily record

VARIABILITY:

Daily variability is usually about 0.5 oC and up to 1 oC during the heating and cooling season.  Data are reported to the nearest 0.5 oC.

BIAS:  Compare with COE data and Richland data

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

Daily mean values can be estimated by averaging the minimum and maximum values where the daily mean values are not available. This record looks precise and representative of the mid Columbia River channel.