COLUMBIA RIVER AT BIGGS, OR. 			   	COMPILED: June 10, 1998 SWM

Revised: July 15, 1998 AL

STATION LOCATION: River mile 208.0 on center span of Route 97 Bridge.

DATA SOURCE: USGS, Oregon District, Portland, OR

BEGINNING DATA: Oct. 1, 1974             ENDING DATE: June. 30,1976        UNITS: Celsius

DATA DESCRIPTION: Daily minimum and maximum values during the 1975-6 water years; total of 643 records.

TITLE OF FILE: cr_biggs.dat                                                               STATION NUMBER: 14048330

COMPLETENESS OF RECORD:

STARTING           ENDING                          COMMENTS	SUSPICIOUS RECORD

10/1/74  --------------- 4/28/75       		daily record

5/12/75  ---------------- 6/6/75      		daily record

6/17/75  -------------- 6/30/76      		daily record

VARIABILITY:

Daily variability is usually 0.5 oC or less and can reach 1.0 oC during the heating and cooling seasons.  Data are reported to the nearest 0.5 oC.

BIAS: The record appears unbiased.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

Daily mean values can be estimated by averaging the maximum and minimum values.  The record appears to be representative of the river cross section and unbiased.