COLUMBIA RIVER NR COLUMBIA CITY, OR. 		            COMPILED: July 16, 1998 AL

Revised: July 17, 1998 SWM

STATION LOCATION: River Mile 82.4 at the head of Deer Island.

DATA SOURCE: USGS, Oregon District, Portland, OR

BEGINNING DATA: Oct. 1, 1970            	 	ENDING DATE: Sept. 30, 1972        UNITS: Celsius

DATA DESCRIPTION: Daily minimum and maximum values; total of about 740 records.

TITLE OF FILE: cr_columbcity1.dat, cr_columbcity2.dat                     STATION NUMBER: 14222890

COMPLETENESS OF RECORD:

STARTING           ENDING                           COMMENTS 		SUSPICIOUS RECORD

10/1/70  -------------- 9/30/72		daily record		10/22/70-4/10/71 biased high

VARIABILITY:

Daily variability is usually about 0.0 to 0.5 oC and up to 1.0 oC during the heating and cooling season.  Data are reported to the nearest 0.5 oC.

BIAS:

For the rainy period from 10/22/70 to 4/10/71, the record is biased 0.5-4oC high, probably influenced by water from the Willamette River.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

The temperatures recorded at this location are probably influenced by water from the Willamette River that has not yet thoroughly mixed with the Columbia River. Daily mean values can be estimated by averaging the minimum and maximum values where the daily mean values are not available.