COLUMBIA RIVER AT INTERNATIONAL BOUNDARY, WA

DATA COMPILED: May 2,1998 AL

Revised: May 29, 1998 SWM

STATION LOCATION: at river mile 745.0, 0.5 miles downstream from Pend Oreille River, on left bank. In 1974, data collection was begun at Northport, 10 miles downstream.

DATA SOURCE: USGS, Washington District, Tacoma, WA

BEGINNING DATA: Oct. 1, 1958		ENDING DATE: Sept. 30,1973	UNITS: Celsius

DATA DESCRIPTION: Daily instantaneous values; total of about 5,470 values.

TITLE OF FILE:  cr-intbound.dat 			STATION NUMBER: 12399500

COMPLETENESS OF RECORD:

START			END			COMMENTS

10/1/58  --------------------- 12/5/58

12/11/58  ------------------ 12/24/58

1/3/59  ------------------------ 2/8/59

2/20/59  --------------------- 4/11/59

6/5/59  ---------------------- 6/22/59

6/29/59  ------------------- 10/21/59

11/8/59  --------------------- 12/4/59

12/14/59  ------------------- 3/20/59

3/28/59  ---------------------- 1/3/61

1/13/61  ---------------------- 4/5/61

4/18/61  ------------------- 11/27/61

12/3/61  --------------------- 6/28/63

7/6/63  ---------------------- 1/21/64

1/28/64  --------------------- 3/26/66

4/7/66  ----------------------- 822/71

8/28/71  --------------------- 9/30/73

VARIABILITY:

Daily variability is usually about 0.5 oC and up to 1 oC during the heating and cooling season.  Data are reported to the nearest 0.5 oC.

BIAS:

Because the Pend Oreille River enters into the Columbia River on the left bank just 0.5 upstream from the sampling point, there is probably a systematic bias to the data collected here, but it appears it may be small.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.  Pacific States Marine Fisheries Council data show 0.1 oC variability between right, mid and left channel readings in 1973.

GENERAL COMMENTS:

Daily mean values can be estimated by averaging the minimum and maximum values where the daily mean values are not available. Temperature data were collected at Northport from 1974-81, and are compatible for that section of river.