COLUMBIA RIVER AT LONGVIEW, WA. 		   DATE COMPILED: July 17, 1998 AL

Revised: July 19, 1998 SWM

STATION LOCATION: River Mile 66 on the north pier of the Longview Bridge, to the right of center channel, 20 miles downstream of Cowlitz River.

DATA SOURCE: USGS, Oregon District, Portland, OR

BEGINNING DATA: Aug. 9, 1967             		ENDING DATE: Sept. 28, 1972        UNITS: Celsius

DATA DESCRIPTION: Daily minimum and maximum values; total of about 1,822 records.

TITLE OF FILE: cr_longview.dat                                                         STATION NUMBER: 14245300

COMPLETENESS OF RECORD:

STARTING           ENDING                          COMMENTS		SUSPICIOUS RECORD

8/9/67  --------------- 5/13/68 		daily record

5/21/68  --------------- 6/3/68       		daily record

6/11/68 ------------- 12/27/68        		daily record

1/8/69  --------------- 1/20/69		daily record

1/31/69  ------------- 6/22/69		daily record

6/28/69  ------------- 7/11/69		daily record

7/17/69  ------------- 10/20/69		daily record

11/18/69  ------------- 1/25/70		daily record

2/3/70  ---------------- 3/24/71		daily record

7/30/71  -------------- 9/27/71		daily record

2/28/72  -------------- 9/30/72		daily record		8/12-8/31/72 biased 0.3-2oC high

VARIABILITY:

Daily variability is usually from 0.0 to 0.5oC and up to 1.0oC during the heating and cooling season.  Data are reported to the nearest 0.5oC. From 1967-69, the data were rounded to the nearest degree Fahrenheit and because of this, they are stepped.

BIAS:

There are no record comparisons to indicate a general bias or not. One exception in 1972 has been noted.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

The record seems unbiased. Daily mean values can be estimated by averaging the minimum and maximum values where the daily mean values are not available.