COLUMBIA RIVER NEAR THE DALLES, OR. 		                COMPILED: July 15, 1998 AL									Revised: July 22, 1998 SWM

STATION LOCATION: at river mile 191.5. Temperatures were taken for conductivity sampling done at The Dalles Dam.  The USGS streamgage station 14105700 is located 2.6 miles downstream at river mile 188.9.

DATA SOURCE: USGS, Oregon District, Portland, OR. Sampling done by USACE Dam personnel.

BEGINNING DATA: October 1, 1957            ENDING DATE: August 8, 1976        UNITS: Celsius

DATA DESCRIPTION: Daily instantaneous values during the 1957-70 and 74-76 water years; total of about 5,786 values

TITLE OF FILE: cr_tdalles.dat                                                          STATION NUMBER: 14105700

COMPLETENESS OF RECORD:

STARTING           ENDING                          COMMENTS		SUSPICIOIUS RECORD

10/12/57  ------------ 9/30/64		daily record		1/12-8/15/58 erratic and biased

10/2/65  -------------- 9/23/70  		daily record

10/1/73  ---------------- 8/8/76       		daily record

VARIABILITY:

Daily variability is unknown.  The entire record is stepped because temperature readings were not made every day.

BIAS:

There may be some inherent bias because most temperature readings were made in conductivity bottles soon after sampling.  Comparison of record with National Marine Fisheries Service data collected in 1968-70 and 74-76 showed an average –0.3 bias in 1968-70 and no bias in the 74-76 record.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Unable to determine.

GENERAL COMMENTS:

Time of measurement is unknown. The quality of the record is fair because the data are stepped and biased.