COLUMBIA RIVER AT UMATILLA, OR. 		              COMPILED: July 15, 1998 AL

Revised:  July 21, 1998 SWM

STATION LOCATION: River mile 290.5 at center span of bridge at Umatilla.

DATA SOURCE: USGS, Oregon District, Portland, OR.

BEGINNING DATA: Oct. 1, 1974             ENDING DATE: Sept. 21,1979        UNITS: Celsius

DATA DESCRIPTION: Daily maximum and minimum values; total of about 1,830 records.

TITLE OF FILE:  cr_umatilla.dat                                                              STATION NUMBER: 14019250

COMPLETENESS OF RECORD:

STARTING           ENDING                          COMMENTS		SUSPICIOUS RECORD

10/1/74  -------------- 10/29/77       		daily record

12/9/77  -------------- 12/31/78      		daily record

1/15/79  --------------- 9/21/79       		daily record

VARIABILITY:

Daily variability is usually 0.5oC or less and can reach 1.0oC during the heating and cooling seasons.  Data are reported to the nearest 0.5oC.

BIAS: Record appears to be unbiased.  1996 record compares well with National Marine Fisheries Service instantaneous record collected in the tailrace of McNary Dam.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

Daily mean values can be estimated by averaging the maximum and minimum values when the daily mean values are not available. Record appears to be representative of the river cross section and unbiased.