GRAND COULEE TDG TAILRACE			DATE COMPILED: March 5, 1998 AL

Revised: April 4, 1998 SWM

STATION LOCATION: at river mile 590.3, on left bank

DATA SOURCE: USACE, Northwestern Division, Portland, OR; data collected by the Bureau of Reclamation

BEGINNING DATA: June 21, 1984		ENDING DATA: Dec. 31, 1997	UNITS: Celsius

DATA DESCRIPTION: From 1984-91, hourly values, 6-12 times per day, and from 1992-97, hourly values for each hour; total of 58,497 values. Daily data file from 1984-97 is 2,395 values. Daily data file includes maximum, minimum, and mean daily values and the variability for the day.

TITLE OF FILE: Daily data: gcgw_tdg84-97d.xls		STATION CODE: GCGW

Hourly data: gcgw_tdg84-97.xls

COMPLETENESS OF RECORD:

START		END		COMMENTS			Suspicious Record

6/21/84 ---------------- 7/31/84	6-12 hourly values per day

4/4/85 ------------------ 8/31/85	6-12 hourly values per day

10/1/85 --------------- 12/12/85	6-12 hourly values per day		record biased –1.0oC

4/1/86 ------------------ 8/31/86	6-12 hourly values per day		record biased –2.0oC

4/21/87 ---------------- 8/31/87	6-12 hourly values per day

4/25/88 ---------------- 8/31/88	6-12 hourly values per day		record biased –1.0oC

4/27/89 ---------------- 8/31/89	6-10 hourly values per day		record biased –1.5oC

4/16/90 ---------------- 8/31/90	6-11 hourly values per day

4/26/91 --------------- 10/31/91	6-11 hourly values per day

4/16/92 ---------------- 10/4/92	6-11 hourly values per day

4/15/93 --------------- 10/12/93	hourly

3/5/94 ------------------ 9/20/94	hourly

4/5/95 ------------------ 9/25/95	hourly

3/8/96 ------------------ 10/7/96	hourly

2/5/97 ---------------- 12/31/97	hourly

VARIABILITY:

Variability is within 0.5oC most of the time.  During the summer season, when there is regulation upstream and variable heating from the sun, the variation within a day can be as great at 2.3oC.

BIAS:

Record with 0.0oC value, >2 times adjacent values, and negative values have been removed. The 1985 record from April 4 to December 12, appears to be biased at least –1.0oC, and from October 1 to December 12, biased as much as –2.0oC. The data  from April 25, 1988 through August 31, 1988 seems biased about –1.5oC.

REPRESENTATIVE OF CROSS SECTION:

Data collected in the tailrace are generally cooler by -0.5 – 1.5oC than downstream temperatures. The data are probably not representative of the mean in the river cross section for this location.

GENERAL COMMENTS:

The record is generally collected seasonally from April to September. It is estimated to be within +0.5oC except for the periods noted under bias. Due to selected withdrawals, temperature of flows released from Lake Roosevelt can be modified relative to incoming flows (Northport gage) up to 5.0oC cooler in June-August, and 2.0 – 4.0oC warmer September-December.