JOHN DAY DAM SCROLL CASE 			DATA COMPILED: July 15, 1998 AL

Revised: July 17, 1998 SWM

STATION LOCATION: at river mile 215.6,taken in the south fishway near diffuser 5 since about 1992. Sensor is at about 11 feet below the water surface.

DATA SOURCE: USACE, Northwestern Division, Portland, OR; data collected by the Portland District

BEGINNING DATA: April 2, 1980             ENDING DATE: Dec. 21, 1997        UNITS: Celsius

DATA DESCRIPTION: Instantaneous daily with some intervening days estimated; total of about 5274 values.

TITLE OF FILE: jda_scr80-97.xls				STATION CODE: JDA

COMPLETENESS OF RECORD:

STARTING           ENDING                          COMMENTS		SUSPICIOUS RECORD

4/2/80 ----------------- 3/14/81            	daily record		entire record biased 1.5oC low

10/2/83 -------------- 12/31/84            	daily record		10/5-11/10/83 biased 1.5oC low

1/1/85  --------------- 12/31/85		daily record		some erratic blips, most days OK

1/1/86  --------------- 12/31/97		scattered values		very erratic record

VARIABILITY:

Variability of data values is unknown. The record is stepped  (the same value is recorded for 5 to 10 days and then a large change is recorded), this makes the record less sensitive to daily variability. A record of very erratic variability from 1986-97.  Temperatures vary as much as + 3oC daily.

BIAS:

Values equal to 0oC, multiples of adjacent values, and negative values removed. Some data is recognizable as biased but most data is too erratic to make an assessment.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Comparison with the Gas Abatement Study of cross-section temperatures for May through August in 1996 and 97, the record is biased from – 2.5 to +1.0 oC; however, much of the time the data is within 0.5 oC.

GENERAL COMMENTS:

A poor record. The data are stepped, much of it is missing, and the remainder is highly variable