JOHN DAY TDG FOREBAY 				DATE COMPILED: July 15, 1998 AL

Revised:  July 17, 1998 SWM

STATION LOCATION: River mile 215.7, in front of powerhouse. Sensor is at a minimum 15-foot depth below water surface.

DATA SOURCE: USACE, Northwestern Division, Portland, OR; data collected by the Portland District

BEGINNING DATA: April 17, 1984                  ENDING DATA: Sept. 16 1997           UNITS: Celsius

DATA DESCRIPTION: Hourly values, 5-24 times per day; total of about 32,571 values.  Daily minimum, maximum, mean, and variability values are calculated; total 2,271 records.

TITLE OF FILE: Daily: jda_tdg84-97d.xls					STATION CODE: JDA

Hourly: jda_tdg84-90.xls, jda_tdg93-97.xls

COMPLETENESS OF RECORD:

START               END                                      COMMENTS		SUSPICIOUS RECORD

4/17/84  ------------- 7/31/84	5-9 hourly values per day		entire record biased 1.5oC high

10/18/84  ---------- 11/29/84 	5-9 hourly values per day		entire record biased 1oC low

3/5/85  --------------- 9/21/86	5-9 hourly values per day		1986 record biased 1oC high

4/17/87  --------------- 9/1/87	5-9 hourly values per day		entire record biased 1oC high

4/23/88  -------------- 9/21/88         	5-9 hourly values per day

4/4/89  --------------- 6/12/89 	5-9 hourly values per day

6/20/89  -------------- 7/9/89  	5-9 hourly values per day

7/19/89  ------------- 8/27/89           	5-9 hourly values per day

4/16/90  ------------- 9/10/90           	5-9 hourly values per day		entire record erratic

no 1991-92 data

4/15/93  -------------- 6/8/93	24 hourly values per day		entire record biased 1.5oC high

6/16/93  ------------- 6/28/93	24 hourly values per day		entire record biased 1.5oC high

1/1/94  -------------- 9/26/94	24 hourly values per day

3/22/95  ------------ 4/20/95	24 hourly values per day

5/9/95  -------------- 9/27/95             	24 hourly values per day

4/1/96  -------------- 9/18/96	24 hourly values per day

3/26/97  ------------ 9/16/97	24 hourly values per day

VARIABILITY:

Original hourly data provided by the USACE were very variable (changes >1.0oC per hour occurred frequently).  Hourly values that were thought to not be representative for the river were deleted; however, it is likely that the remaining record is still poor and the resulting values can only be considered to be within +1oC of representative river temperatures.  The temperatures collected at the nearby tailrace station (JHAW) are more representative of the river, but the record length is much shorter.

BIAS: Data were erratic and were biased as noted. The 1994-97 data seemed to show no bias.

REPRESENTATIVE OF CROSS SECTION:

The forebay record compared to the Gas Abatement Study during May and August 1997 show 0.0 to +0.3oC bias.  However because of the high variability at this site (see variability), the summer months of June through September can be biased higher than 0.3oC at times.

GENERAL COMMENTS:

The data recorded here seem to follow the 1984-91 data collected at The Dalles forebay (TDA) very closely at times and may be the same record.  For dates with no time listed in the 1984-90 period, an hour of 0000 was assumed for the time of collection.  The early record from 1984-90 is poor, but the record from 1994-97 seems without bias. Lowering the position of the thermister (placing at greater depth) may provide a more representative measurement of temperature with respect to the river cross section.