COLUMBIA RIVER AT KALAMA, TDG  			DATE COMPILED: July 16, 1998 AL

Revised: July 17, 1998 SWM

STATION LOCATION: River mile 77 at Harvest States Corp. dock on right bank. The sensor is a minimum 15 feet below the water surface.

DATA SOURCE: USACE, Northwestern Division, Portland, OR; data collected by the Portland District

BEGINNING DATA: June 22, 1993	ENDING DATA: Sept. 19, 1997	UNITS: Celsius

DATA DESCRIPTION: Hourly values, usually 24 values per day, total 18,105 values.  Daily data includes daily maximum, minimum, mean, and variability for the day, total 759 records.

TITLE OF FILE: Daily: klaw_tdg93-97d.xls				STATION CODE: KLAW

Hourly: klaw_tdg93-97.xls

COMPLETENESS OF RECORD:

START		END		COMMENTS		SUSPICIOUS RECORD

6/22/93  ------------ 9/4/93		24 values per day

3/28/94  ---------- 9/24/94		24 values per day		entire record biased 1-4oC low

3/24/95  ---------- 9/28/95		24 values per day		8/30-9/5/95 biased 0.4-0.8oC high

5/29/96  ---------- 9/16/96		24 values per day

3/6/97  ----------- 9/19/97		24 values per day

VARIABILITY:

Daily variability about the daily mean is between 0.1 and 0.4 oC most of the time.

BIAS: The KLAW record appears to be biased high .3 to .5oC relative to the cross section of the Columbia River during July and August 1995, and July 1996.  There was no apparent bias in the July 97 comparative record.  This bias is potentially present during the June through September time period.

REPRESENTATIVE OF CROSS SECTION:

The record appears to be biased high 0.3 to 0.5oC relative to the cross section of the Columbia River during July and August 1995, and July 1996.  There was no apparent bias in the July 97 comparative record

GENERAL COMMENTS:

This record is estimated to be biased high during the June through September period and the daily mean values to be within 0.5 oC of maximum and minimum values recorded.