KALAMA RIVER NEAR KALAMA, WA.			DATE COMPILED: June 10, 1998 SWM

Revised: July 20, 1998 AL

STATION LOCATION: River mile 2.8 on the right bank at bridge.

DATA SOURCE: USGS, Washington District, Tacoma, WA

BEGINNING DATA: May 21, 1970             		ENDING DATE: Sept. 28, 1979        UNITS: Celsius

DATA DESCRIPTION: Daily maximum and minimum values 1970-78 water years; daily maximum, minimum, and mean values 1979 water year; total of about 3,422 records.

TITLE OF FILE: kalama_r.dat                                                               STATION NUMBER: 14223600

COMPLETENESS OF RECORD:

STARTING           ENDING                          COMMENTS		SUSPICIOUS RECORD

5/21/70  ---------------- 9/2/70		daily max, min record

9/8/70  ---------------- 11/17/70       		daily max, min record

7/16/70  --------------- 2/16/72          		daily max, min record

2/22/72  --------------- 9/30/73		daily max, min record

2/13/74  ---------------- 8/1/74       		daily max, min record

8/9/74    --------------- 10/1/74      		daily max, min record

10/15/74  -------------- 12/1/77		daily max, min record

4/12/78  ---------------   9/8/78		daily max, min record

9/8/78  ---------------  12/19/78		daily max, min, mean record

1/4/79  ----------------- 1/21/79		daily max, min, mean record

2/1/79  ----------------- 4/20/79		daily max, min, mean record

5/8/79  ----------------- 6/23/79		daily max, min, mean record

7/10/79  ---------------- 9/28/79		daily max, min, mean record

VARIABILITY:

Daily variability is usually about 1-2oC, but can be as high at 4oC during the heating and cooling seasons. Day-to day variability of the mean can also be high; usually from 0-2oC. Data are reported to the nearest 0.5oC. The temperature record for the Kalama River has some similarity to the Cowlitz River but it has a greater day-to-day and daily variability.

BIAS:

Unable to determine because no comparable continuous record for these time periods is available. In general, the Kalama River runs at about the same temperature level as the Cowlitz River. When records can be compared, the temperature record for the Kalama River is slightly warmer by about 0-2oC from April through July, and cooler by about 1-5oC from September through November.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

The record appears to be good. Daily mean values can be estimated by averaging the maximum and minimum values when the daily mean values are not available.