LOWER GRANITE DAM TDG TAILRACE 	 	  COMPILED: July 10, 1998 SWM

Revised: July 31, 1998 AL

STATION LOCATION: River mile 106.8, 0.75 miles downstream of Lower Granite Dam, on right bank.

DATA SOURCE: USACE Western Division, Portland, OR, data collected by Walla Walla District

BEGINNING DATA: April 10, 1995		ENDING DATA: Sept. 17, 1996	UNITS: Celsius

DATA DESCRIPTION: Hourly values collected usually include 24 values per day.  Data file has about 7,000 hourly values.  Data file also includes daily maximum, minimum, and mean values and the variability about the daily mean; total 342 records.

TITLE OF FILES: Hourly: lgnw_tdg95-96.xls				STATION CODE: LGNW

Daily: lgnw_tdg95-96d.xls

COMPLETENESS OF RECORD:

START		END			COMMENTS			SUSPICIOUS RECORD

4/10/95  ----------- 9/26/95			hourly and daily values

4/2/96  ------------ 9/17/96			hourly and daily values	6/1-7/27/96 biased 0.2-2.5oC low

1997 data missing

VARIABILITY:

Daily variability is between 0.1 and 0.4 oC most of the time. This record has very little variability within a day.

BIAS:

The record appears to be biased high 1.0 to 1.4oC during May 1995 and biased high 1.3 to 1.5oC during June 1995 relative to cross sectional measurements. With respect to the LGSW record, the LGNW record is biased high 0.2-1.5oC high in 1995 and 0.2-2.5oC low in 1996.

REPRESENTATIVE OF CROSS SECTION:

Cross sectional data showed the river to be mixed within 0.2oC and this location should be representative of the river except measurements are biased much of the time.

GENERAL COMMENTS:

The record is generally collected seasonally from April to September. The measuring section should be representative but the record has significant instrument bias. This record is identical to the LMNW record.