LOWER MONUMENTAL DAM SCROLL CASE 			COMPILED: July 31, 1998 SWM

Revised: July 31, 1998 AL

STATION LOCATION: River mile 41.6 at unit 1 cooling water at 120-foot depth.

DATA SOURCE: USACE, Northwestern Division, Portland OR; data collected by the Walla Walla District

BEGINNING DATA: Nov. 1, 1974	 	ENDING DATE: Oct. 31, 1996		UNITS: Celsius

DATA DESCRIPTION: Instantaneous daily with some intervening days missing and some estimated; total of 3,550 values

TITLE OF FILE: lmn_scr74-79,88-96.xls				STATION CODE: LMN

COMPLETENESS OF RECORD:

STARTING	ENDING	COMMENTS

11/1/74  ------------- 4/30/79	daily record

5/10/88 ------------ 10/29/88	scattered values		1980-87 record missing

4/4/89  ------------- 10/23/89	scattered values

5/2/90 --------------- 11/1/90	daily record

4/2/91 --------------- 11/1/91	daily record

4/2/92 -------------- 11/1/92	daily record

4/1/93  ------------- 11/30/93	daily record

4/1/94  ------------- 10/31/94	daily record

4/1/95  ------------- 10/31/95	daily record

4/1/96  ------------- 10/31/96	daily record		1997 record missing

VARIABILITY:

No measure of daily variability made. The record is stepped  (the same value is recorded for 5 to 10 days and then a large change is recorded), this makes the record less sensitive to daily variability.

BIAS:  The record was biased from +0.5 to – 0.5oC relative to the Gas Assessment Study data in May 1996. It is difficult to assess bias because of the stepping. When compared to the USGS gage at Burbank and tailrace data, the scroll-case data are generally within +1oC.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

No representative assessment has been made.

GENERAL COMMENTS:

The record from 1974 through 1979 if fairly complete with a few days with no data.  The record during 1988 and 1989 has less than 50 percent of the values present. The 1990 through 92 data are recorded on a daily basis with no attempt to fill in missing readings with previous data (this normally gives a stair-step record with the same value repeated for several days); the 1993-96 record is stepped also. Although the record is stepped, it does appear to be within +1oC.