LOWER GRANITE DAM TDG FOREBAY	 		DATE COMPILED: July 10, 1998 SWM

Revised:  July 31, 1998 AL

STATION LOCATION: River mile 107.5 on outside of wall to navigational lock upstream of spillway

SOURCE OF DATA: US Army Corps of Engineers Pacific Division Office, data collected by Walla Walla District Office.

BEGINNING DATA: May 30, 1988                  ENDING DATA: Sept. 17, 1996           UNITS: Celsius

DATA DESCRIPTION: Hourly values, usually 6 times per day for 1988 through 90 and 24 hourly values in 91 through 96; total of about 24,000 values.  Daily minimum, maximum, mean, and variability statistics are available; total 1,359 records.

TITLE OF FILE: Hourly: lwg_tdg88-92.xls, lwg_tdg93-96.xls			STATION CODE: LWG

Daily: lwg_tdg88-96d.xls

COMPLETENESS OF RECORD:

START               END                      	COMMENTS

5/30/88  ------------- 9/22/88		hourly and daily values	1984-87 data missing

4/5/89  -------------- 9/12/89		hourly and daily values

4/16/90  ------------ 5/25/90		hourly and daily values

6/10/90  ------------ 6/26/90		hourly and daily values

7/9/90  -------------- 10/4/90		hourly and daily values

4/10/91  ------------- 11/5/91		hourly and daily values

2/27/92  -------------- 3/8/92		hourly and daily values    		most of 1992 data missing

4/9/93  -------------- 9/28/93		hourly and daily values

4/1/94  -------------- 9/28/94		hourly and daily values

4/1/95  -------------- 9/30/95		hourly and daily values

4/2/96  -------------- 9/17/96		hourly and daily values		biased 0.5-1.5oC low

VARIABILITY:

Daily variability about the daily mean is usually between .2 and 1.0 but can be over 2.0 oC.  When the variability is greater than about 0.7 oC, it is likely that it is the result of high values that may not be representative of the cross section and may result in a daily mean value being biased high.

BIAS:

When there is high hourly variability, it can result in variable daily means and/or daily mean values biased high by 1.0 oC or more. Data appears relatively unbiased except as noted.

REPRESENTATIVE OF CROSS SECTION:

Not known.

GENERAL COMMENTS:

The record is generally collected seasonally from March or April to September. Record correlation with tailrace data (which is very short) show the forebay record to be relatively unbiased most of the time.