MCNARY DAM SCROLL CASE 		                        DATA COMPILED: July 14, 1998 AL

Revised: July 17, 1998 SWM

STATION LOCATION: River mile 292.0 sensor located in Unit 1 of powerhouse at cooling water system at 40 foot depth; if unit 1 is off, the sensor at unit 2 is read.

SOURCE OF DATA: Northwestern Division, USACE, Portland, OR; collected by Walla Walla District.

BEGINNING DATA: Nov. 1, 1974             ENDING DATE: Dec 31, 1997        UNITS: Celsius

DATA DESCRIPTION: Instantaneous daily data with many intervening days estimated (causing a stepped record) and some days with more than one value; total of 7,864 values

TITLE OF FILE: mcn_scr74-97				STATION CODE: MCN

COMPLETENESS OF RECORD:

STARTING           ENDING                       COMMENTS		SUSPICIOUS RECORD

11/1/74   --------------- 3/14/81      	one value per day at 7-8:00hrs	much missing record

no 1982 data							3/1-8/31/80 biased 0.5-1oC low

10/2/83  ---------------- 3/25/87      	one value per day at 7-8:00hrs

1/2/88    ---------------- 4/20/88      	one value per day at 7-8:00hrs

5/30/88  --------------- 12/31/97        	one or more values per day

VARIABILITY:

The record is stepped  (the same value is recorded for 5 to 10 days and then a large change is recorded), this makes the record less sensitive to daily variability.

BIAS:

Values equal to 0oC, multiples of adjacent values, and negative values have been removed. It is difficult to assess bias because of the stepping and because large blocks of data are missing, but the period from March 1 to September 1, 1980 seems biased low by about 0.5 to 1.0oC.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Comparison of the record with the Gas Assessment Study record in April, May, and August 1997 shows no prevailing bias, and except for the stepped nature of the record which lead to disagreement of up to 1.0oC, the scroll-case data seems to be fairly representative of the cross-section data.

GENERAL COMMENTS:

Because of the stepped nature of this record throughout, and because there are many periods of missing record, it is not considered a good record.