MCNARY TDG FOREBAY (OREGON SIDE OF DAM)	   DATE COMPILED: July 13, 1998 AL

Revised: July 17, 1998 SWM

STATION LOCATION: at river mile 292.1, upstream of dam near left bank near powerhouse. Sensor is at a minimum 15 feet depth below water surface.

DATA SOURCE: USACE, Northwestern Division, Portland, OR; collected by the Walla Walla District.

BEGINNING DATA: April 2, 1985	ENDING DATA: Dec. 31, 1997		UNITS: Celsius

DATA DESCRIPTION: Daily values, total of 2,535 values.		STATION CODE: MCQO

Hourly values, total of 41,115 values

TITLE OF FILE: Daily: mcqo_tdg85-97d.xls

Hourly: mcqo_tdg85-92.xls, mcqo_tdg93-97.xls

COMPLETENESS OF RECORD:

START               END                            COMMENTS			SUSPICIOUS RECORD

4/2/85  --------------- 8/31/85	5-9 hourly values per day		6/27-7/28 biased 1-2oC high

10/30/85  -----------12/12/85	5-9 hourly values per day		10/30-12/12 biased 0.5-1oC low

several days with high variability

4/1/86  ---------------- 9/4/86	5-9 hourly values per day		6/25-9/4 biased 0.5oC high

4/29/87  --------------- 9/1/87	5-9 hourly values per day

4/22/88  ------------- 9/22/88	5-9 hourly values per day		entire period about 0.5oC low

4/3/89  --------------- 9/11/89	5-9 hourly values per day

416/90  -------------- 6/20/90	5-9 hourly values per day		entire period 1-2oC low

6/26/90  ------------- 9/10/90	hourly and daily values 		several days with high variability

entire period 1-2 oC low

4/18/91  ------------- 10/7/91	5-9 hourly values per day

4/16/92  ------------- 9/24/92	generally 24 hourly values per day	entire period 0.5-1oC low

4/21/93  ------------- 9/12/93	generally 24 hourly values per day

3/21/94  ------------- 9/26/94	generally 24 hourly values per day

1/1/95  --------------- 9/26/95	generally 24 hourly values per day

4/1/96  ------------- 12/13/96	generally 24 hourly values per day	4/1-7/13 biased about 1oC low

7/20-11/13 biased 1-2oC high

2/11/97  ------------ 12/31/97	generally 24 hourly values per day	several days with high variability

VARIABILITY: Original hourly data provided by the US Army Corps of Engineers was very variable (>1.0oC per hour about the daily mean).  Hourly values that were thought to not be representative of the whole river were deleted.  It is likely that the resulting daily mean values are usually within 1.0oC, but at times could be different by 2.0oC from the true river value.  The tailrace station, MCPW, is thought to be representative of the whole river. This record has more problems with variability than the Washington record, WCQW.

BIAS: Records with 0oC value, > 2 times adjacent values, and negative values have been removed.  Data are somewhat erratic and seem to have bias at times (refer to suspicious record comments).

REPRESENTATIVE OF CROSS SECTION: Comparison of this record with the Gas Assessment Study data for April, May, and August 1997, shows no persistent bias.  However because of the large daily variability and amount of record that has been deleted because it is though to not be representative of the river, the daily mean record from this site could be in error by 1 to 2oC relative to the true temperature.

GENERAL COMMENTS: Data seem to show more variability than would be expected and appear to have significant bias in the years 1985, 86, 88, 90, 92, and 96.