ROCKY REACH TDG FOREBAY			DATE COMPILED: Mar. 29, 1998 SWM

Revised: April 28, 1998 AL

STATION LOCATION: at river mile 473.8, on right side of dam

DATA SOURCE: USACE, Northwestern Division, Portland, OR; data collected by Chelan PUD

BEGINNING DATA: April 26, 1984	ENDING DATA: Sep. 30, 1997	UNITS: Celsius

DATA DESCRIPTION: Hourly values, 3-6 times per day; total of about 3,440 values (1984-90), and hourly (1996-97), 405 values.

TITLE OF FILE: Daily data: rrh_tdg84-89d.xls and rrh_tdg93-97d.xls		STATION CODE: RRH

Hourly data: rrh_tdg84-89.xls and rrh_tdg93-97.xls

COMPLETENESS OF RECORD:

START			END		COMMENTS		Suspicious Record

4/26/84  ------------------- 8/1/84	3-6 hourly values per day

5/10/85  ------------------- 7/1/85	3-6 hourly values per day

4/14/86  ------------------ 7/16/86	3-6 hourly values per day

4/15/87  ------------------ 7/16/87	3-6 hourly values per day

missing 1988 record

4/2/89  ------------------- 7/28/89	3-6 hourly values per day

missing 1990-92 record

4/16/93  ------------------ 7/21/93	3-6 hourly values per day

4/15/94  ------------------ 6/18/94	3-6 hourly values per day

5/2/95  ------------------- 9/16/95	3-6 hourly values per day

3/1/96  ------------------ 10/15/96	3-6 hourly values per day

4/2/97  ------------------- 9/30/97	hourly values			biased up to –2.0oC

VARIABILITY:

1984-90, 96-97 data -- Variability is less than 0.5 oC most of the time.  During the summer season, when there is regulation upstream and variable heating from the sum, the variation within a day can be as high as 1.0 oC.

BIAS:

Records with values  > 2 times adjacent values have been removed. Record appears to be good and to have no bias except for the year 1997 when there appears to be as much as –2.0oC.

REPRESENTATIVE OF CROSS SECTION:

Comparison of data made available by Pacific States Marine Fisheries Council collected in 1966, 71, and 72 at the forebay spillway and mid channel showed no bias for either site; minimum, median, and maximum variability within the cross section was 0.0, 0.2, and 0.8oC.

GENERAL COMMENTS: In general, temperatures are slightly cooler, sometimes as much as 0.5oC from scroll case temperatures. Temperatures are recorded at a minimum depth of 10 feet.