WANAUM SCROLL CASE				DATA COMPILED: April 23, 1998 SWM

Revised: May 27, 1998 AL

STATION LOCATION: at river mile 415.8. Since 1989, the same as Priest Rapids scroll-case.

BEGINNING DATA: June 2, 1981		ENDING DATE: Nov. 15, 1997	UNITS: Celsius

DATA DESCRIPTION: Instantaneous daily with some intervening days estimated; total of 3,624 values

TITLE OF FILE: wan_scr81-97.xls		STATION CODE: WAN

COMPLETENESS OF RECORD:

START			END	COMMENTS

6/2/81 ----------------- 12/11/81      	daily record

3/2/82 -------------------- 1/5/84      	daily record

4/2/84  ---------------- 11/20/84        	daily record

4/2/85  ------------------ 12/1/85      	daily record

4/3/86  ------------------ 12/1/86       	daily record

4/17/87 ----------------- 12/1/87 	daily record

4/17/88 ----------------- 12/1/88        	daily record

Record is collected at Priest Rapids Dam from 1989 to present

4/17/89 ---------------- 11/16/89        daily record

4/23/90 ---------------- 11/16/90      	daily record

5/15/91  --------------- 11/16/91      	daily record

4/25/92  --------------- 11/13/92       	daily record

4/16/93  ----------------- 6/21/93       	daily record

4/17/94  ---------------- 5/19/94       	daily record

4/15/95  --------------- 11/15/95       	daily record

4/16/96  --------------- 10/31/96       	daily record

4/15/97  --------------- 11/15/97       	daily record

VARIABILITY:

Unable to determine variability within a day with once-a-day values. The data are stair stepped from 1981-88 which reduces variability on a day-to-day basis.

BIAS:

Values equal to 0 oC, multiples of adjacent values, and negative values have been removed.  No periods of bias noted.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Comparison of data collected in 1966 at the Wanapum forebay and reported by Pacific States Marine Fisheries Council (PSMFC) showed a minimum, median, and maximum of variability of 0.2, 0.5, and 1.7 oC respectively.  Comparison of PSMFC data collected in 1971 from the forebay and stilling basin showed no bias between the two sites.  Comparison of data provided by PSMFC data for 1972 at Wanapum forebay units 11 and 5, tailrace, powerhouse, and below Crab Creek showed some positive bias at forebay unit 11 and Crab Creek, with a median differences of 0.3 oC.

GENERAL COMMENTS:

Prior to 1989, the record was collected at the Wanipum Dam scroll case and was stair stepped. From 1989, the data were collect at the Priest Rapids Dam scroll case.