WANAUM  TDG TAILWATER				DATA COMPILED: April 23, 1998 SWM

Revised: May 27, 1998 AL

STATION LOCATION: at river mile 415.9 in mid-channel near left bank.

BEGINNING DATA: April 1, 1995		ENDING DATE: Dec. 31, 1997	UNITS: Celsius

DATA DESCRIPTION Hourly data; total of 33,365 values, daily data total of 602 values.

TITLE OF FILE: Daily data: wan_tdg_tail93-97d.xls		STATION CODE: WAN

Hourly data: wan_tdg_tail93-97.xls

COMPLETENESS OF RECORD:

START			END	COMMENTS		Suspicious Record

5/17/93  ---------------- 6/21/93       	Hourly values

3/29/94  ---------------- 5/22/94       	Hourly values

4/1/95  ----------------- 12/31/95       	Hourly values		Entire 1995 period deleted

3/22/96  --------------- 10/17/96       	Hourly values		June-August biased high

3/13/97  --------------- 12/31/97       	Hourly values

VARIABILITY:

Variability is less than 0.5oC most of the time.  During the summer season, when there is regulation upstream and variable heating from the sum, the variation within a day can be as high as 1.0oC.

BIAS:

Values equal to 0 oC, multiples of adjacent values, and negative values have been removed.  The entire 1995 period was biased high and showed more variability than nearby records so it was deleted. The period June-August, 1996 was biased high.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Comparison of data collected in 1966 at the Wanapum forebay and reported by Pacific States Marine Fisheries Council (PSMFC) showed a minimum, median, and maximum of variability of 0.2, 0.5, and 1.7 oC respectively.  Comparison of PSMFC data collected in 1971 from the forebay and stilling basin showed no bias between the two sites.  Comparison of data provided by PSMFC data for 1972 at Wanapum forebay units 11 and 5, tailrace, powerhouse, and below Crab Creek showed some positive bias at forebay unit 11 and Crab Creek, with a median differences of 0.3 oC.

GENERAL COMMENTS:

Record seems to be good except those noted as biased.