COLUMBIA RIVER AT WAUNA MILL TDG  		DATE COMPILED: June 7, 1998SWM

Revised: July 17, 1998

STATION LOCATION: River mile 42 at James River Co. dock on left bank. The sensor is a minimum 15 ft below the water surface.

DATA SOURCE: USACE, Northwestern Division, Portland, OR; data collected by the Portland District

BEGINNING DATA: July 3, 1993	ENDING DATA: Sept. 19, 1997	UNITS: Celsius

DATA DESCRIPTION: Hourly values, usually 24 values per day, total 20,633 values.  Daily data includes daily maximum, minimum, mean, and variability for the day, total 1,025 records.

TITLE OF FILE: Daily: wano_tdg93-97d.xls			STATION CODE: WANO

Hourly: 	wano_tdg93-97.xls

COMPLETENESS OF RECORD:

START		END		COMMENTS		SUSPICIOUS RECORD

7/3/93  ------------ 7/21/93		24 values per day

8/19/73  ------------ 9/7/93		24 values per day

3/19/94  ---------- 8/11/94		24 values per day		3/30-7/15/94 biased 1-2.5oC high

8/17/94  ---------- 9/23/94		24 values per day

3/8/95  ------------- 1/8/96		24 values per day		3/12-7/16/95 biased 0.5-1oC high

3/6/96  ------------ 4/22/96		24 values per day

6/2/96  ------------ 8/10/96		24 values per day

8/16/96  ---------- 9/20/96		24 values per day

3/4/97  ------------ 9/19/97		24 values per day		entire 1997 period biased 0.5-2oC high

VARIABILITY:

Daily variability about the daily mean is between 0.1 and 0.4oC most of the time.  The variability is often greater during the warmer months and when there have been calibration changes, especially during the 93-95 years.

BIAS:

During May and August 1995 and July 96 and 97, the WANO record is biased high between .3 and 1.0oC relative to the cross section of the Columbia River. The temperatures measured are not representative of the average temperature of the river probably because sampling is done in a warmer part of the river.

REPRESENTATIVE OF CROSS SECTION:

During May and August 1995 and July 96 and 97, data from within the river channel showed the WANO record to be more variable than sites in the river and biased high between 0.3 and 1oC.

GENERAL COMMENTS:

The record is poor and estimated only to be within – 0.5 and + 2oC of the mean for the river cross section The record is biased high 0.3 to 1oC during much of the record collected between May and September.  The variability decreases and the bias is unknown during other months.