WELLS SCROLL CASE					DATA COMPILED: 4/2/98 AL

Revised:  4/28/98 SWM

STATION LOCATION: at river mile 515.6, in center of dam

BEGINNING DATA: May 2, 1980		 ENDING DATE: November 15, 1997	UNITS: Celsius

DATA SOURCE: USACE, Northwestern Division, Portland, OR

DATA DESCRIPTION: Instantaneous daily with some intervening days estimated and some days with more than one value; total of 2,750 values

TITLE OF FILE: wel_scr80-97.xls			STATION CODE: WEL

COMPLETENESS OF RECORD:

START		      END		COMMENTS

5/2/80 ------------- 11/23/80	daily record

10/2/83 ------------- 12/1/83	daily record

5/2/84 ------------- 11/26/84	daily record	From 8/21 to 10/1 data appear to be about 0.5oC low

5/2/85 ------------- 11/23/85	daily record

5/2/86 ------------- 11/17/86	daily record

1987 data is missing

5/2/88 --------------- 8/21/88	daily record

9/1/88 --------------- 11/1/88	daily record

5/2/89 ------------- 11/23/89	daily record

5/2/90 -------------- 11/8/90		daily record

5/9/91 ------------- 11/16/91	daily record

5/2/92 ------------- 11/16/92	daily record

5/1/93 --------------- 11/8/93	daily record

5/1/94 ------------- 11/15/94	daily record

5/1/95 ------------- 11/31/95	daily record

7/2/96 ------------- 11/15/96	daily record

5/1/97 ------------- 11/15/97	daily record

VARIABILITY:

No daily variability assessment made. From 1980-97, data were generally collected at 24:00 with some values listed at 07:00 and 15:00 times.  Data are stepped and are therefore less sensitive to variability on a day-to-day basis.

BIAS:

Values equal to 0.0oC, multiples of adjacent values, negative values, and outlyers have been removed. The bias is estimated to be generally about 0.2oC higher than the total dissolved gas data collected in the forebay.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

No data could be found to measure how representative the monitoring data was of the river cross section.

GENERAL COMMENTS:

The record is generally stair-stepped and takes some uncharacteristic dips and blips. Some data look to be recorded from readings made on previous days (this normally gives a stair-step record with the same value repeated for several days). There are peaks and troughs that may not be characteristic of the mean temperature of the cross section. The Well scroll case data tend to run higher than the forebay data through most of the year for most years. Data are collected at a depth of about 10 feet and from the center of the river channel just off forebay pier noses.