WILLOW CREEK NR ARLINGTON, OR. 			DATE COMPILED: June 10, 1998 SWM

Revised: July 20, 1998 AL

STATION LOCATION: River mile 3.7 at gaging station on right bank at bridge.

DATA SOURCE: USGS, Oregon District, Portland, OR

BEGINNING DATA: November 25, 1963            	ENDING DATE: April 8, 1968        UNITS: Celsius

DATA DESCRIPTION: Daily instantaneous observer readings, often with many missing days, during the 1964-68 water years; total of about 1,601 records.

TITLE OF FILE: willow_cr.dat                                                               STATION NUMBER: 14036000

COMPLETENESS OF RECORD:

STARTING           ENDING                           COMMENTS			SUSPICIOUS RECORD

11/25/63  -----------  6/21/64		inst. daily record – scattered	high variability

10/8/64  -------------  7/30/66       		inst. daily record – scattered	high variability

11/2/66 -------------- 7/27/67        		daily record

7/28//67  ------------- 4/8/68		daily record -- scattered

VARIABILITY:

Daily variability is not definable. Day-to day variability of the mean can be high; usually from 0-5oC.  Data are reported to the nearest 0.5oC. The temperature record for Willow Creek has some similarity to the John Day River but it has a greater day-to-day and daily variability. The instantaneous data collected on Willow Creek has a large day-to-day variability. Daily instantaneous readings do not reflect a mean temperature and are subject to the time of day they are taken. Consequently, they can be much higher or lower than the mean.

BIAS: Unable to determine because no comparable record in the area; however, the entire data collection period should be viewed with suspicion. In general Willow Creek runs at about the same temperature level as the John Day River. When records can be compared, the temperature record for Willow Creek is slightly warmer by about 0-2oC throughout the year.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

Temperature data were collected on an instantaneous basis and thus have a high variability. These records are not as good as maximum, minimum data.