WILLAMETTE RIVER AT OREGON CITY 		DATE COMPILED: June 10, 1998 SWM

Revised: July 20, 1998 AL

STATION LOCATION: River mile 27.8 on the right bank.

DATA SOURCE: USGS, Oregon District, Portland, OR.

BEGINNING DATA: March 23, 1963             ENDING DATE: September 30, 1967        UNITS: Celsius

DATA DESCRIPTION: Daily maximum and minimum values during the 1963-67 water years; total of about 1,657 records.

TITLE OF FILE: wr_orcity.dat                                                               STATION NUMBER: 14207700

COMPLETENESS OF RECORD:

STARTING           ENDING                           COMMENTS		SUSPICIOUS RECORD

3/23/63  -------------- 3/12/64 		daily record

3/20/64  -------------- 4/15/64       		daily record

4/323/64 -------------- 7/17/64        		daily record

7/23/64  ------------- 11/21/65		daily record

12/9/65  ------------- 10/19/66    		daily record

10/27/66  ------------ 10/31/66		daily record

11/8/66  ------------- 11/21/66		daily record

11/29/66  ------------ 1/23/67		daily record

2/7/67  --------------- 9/30/67           		daily record

VARIABILITY:

Daily variability is usually from 0.0-0.5oC and up to 1.5oC during the heating and cooling season. Day-to day variability of the mean is usually from 0-1oC. Data are reported to the nearest 0.5oC. The daily and day-to-day variability is low primarily because of stream size and depth, but also because of constant groundwater, snowmelt, and glacial inflows.

BIAS:

Unable to determine because no comparable continuous records were available for this area. Temperatures are consistently warmer that those in the Deschutes and Cowlitz Rivers.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

The record seems to be good. Daily mean values can be estimated by averaging the minimum and maximum values where the daily mean values are not available.