WILLAMETTE RIVER AT PORTLAND, OR. 		DATE COMPILED: June 10, 1998 SWM

Revised: July 20, 1998 AL

STATION LOCATION: River mile 12.8 on the left pier of the Morrison Bridge.

DATA SOURCE: USGS, Oregon District, Portland, OR

BEGINNING DATA: Nov. 7, 1975             	ENDING DATE: 9/30/81        UNITS: Celsius

DATA DESCRIPTION: Daily maximum and minimum values 1977-78 water years; daily maximum, minimum, and mean values 1979-81 water years; total of about 2,159 records.

TITLE OF FILE: wr_portland.dat                                                             STATION NUMBER: 14211720

COMPLETENESS OF RECORD:

STARTING           ENDING                          COMMENTS

11/7/75  -------------- 6/18/77 		daily max, min record

7/1/77  -------------- 11/25/77       		daily max, min record

1/12/78 ----------------  9/7/78		daily max, min record

9/8/78  ---------------  8/27/80        		daily max, min, mean record

9/3/80  ---------------- 9/30/81		daily max, min, mean record

VARIABILITY:

Daily variability is usually from 0.0-0.5oC and up to 1.5oC during the heating and cooling season. Day-to day variability of the mean is usually from 0-1oC. Data are reported to the nearest 0.5oC. The daily and day-to-day variability is low primarily because of stream size and depth, but also because of constant groundwater, snowmelt, and glacial inflows.

BIAS:

Unable to determine because no comparable continuous records were available for this area. Temperatures are consistently warmer that those in the Deschutes and Cowlitz Rivers.

MONITORING SITE REPRESENTATIVE OF CROSS SECTION:

Part of the USGS protocol was to insure the data were representative of the cross section.

GENERAL COMMENTS:

The record seems to be good. Daily mean values can be estimated by averaging the minimum and maximum values.